## Slide 1
FPGA ADC Design Queries

## Slide 2
Understanding the Input Sources.
Different Sensors used in the Setup and their data sheets?
According to a video on your You tube channel (link: https://www.youtube.com/watch?v=3hnkpcPnxD4), we understood there are multiple conveyer belts, one of the conveyer belt where robot is picking and placing the selected objects is for determining the length, thickness of the object or is there any other sensor at a different conveyer belt from where the input to the system is captured?
If you could share a similar video of the setup will help understand the entire process?
The Sensor type and their data sheets will help us understand
Sensor for distance measurement shared is Baumer OM20-P0120, this sensor provides distance to the object to be measured is calculated from the location of the image on the receiver element. The measured distance is provided as a measured value via the following channels integrated in the sensor:
    1. Digital IO-Link interface
    2. Analog output
    2a. Analog measurement field : This is defined by max and min distance configured as shown in the figure below (Pg. 36 document Baumer_OM20- 30-IO-Link_EN_V6_MNL.pdf)

## Slide 3: Understanding the Input Sources cont…
    2b. Measurement rate: The measuring frequency value depends on the exposure time.
    3b. Response delay:
    4b. Histogram Data:
    6. Are the input channels fast switching or not?

## Slide 4: Understanding ADC
The last question from the previous slide will help decide on the type of ADC to be used Delta-Sigma or SAR type ADC?
Delta-Sigma ADC, as the delta-sigma ADC shapes the quantization noise such that most of it occurs outside the bandwidth of interest, resulting in increased overall dynamic range at low frequencies and reduces the weight on Anti-aliasing filter as well
The above process is performed by Oversampling and decimation of the output received from ADC, the only problem when we are selecting an external ADC is that the Oversampling process needs to be implemented as a software or in FPGA block and converting it to a 16-bit as an input for FIR filter.
ADC selected is 100sps (Delta-Sigma type)

## Slide 5: Proposed Block Diagram
PGA
AAF
ADC
FIR FILTER
PGA
AAF
ADC
Over sampling and Decimation filter
FIR FILTER
PGA
AAF
ADC
FIR FILTER
PGA
AAF
ADC
FIR FILTER
M
U
X
SPI INTERFACE
Master
Analog Front End
FPGA or Digital End
Over sampling and Decimation filter
Over sampling and Decimation filter
Over sampling and Decimation filter

## Slide 6: Existing Quick Filter SPI design:
The SPI used in the Quick filter uses a control block that helps decide which channel/s to select for data capture from the FIR block.
There are three modes of operation for SPI namely
  Wait mode
  Run mode (Transmits all zeros)
  Halt mode
There are various register setting that take place during the transfer and monitoring of the SPI transfer.
The Signals used in the SPI transfer are
  DRDY signal
  /CS signal
  sclk
  SI
  SO

## Slide 7: Pin Mapping for SPI control
DRDY signal
SSn Pin
sclk generation

## Slide 8
DRDY identification

## Slide 9
References
740-xxxxx Analog Filter Board.docx
QF4A512revD6.pdf
QFAN001-Interfacing to the QF4A512 Digital SPI port.pdf
https://www.ti.com/video/6301516529001